## Slide 1
Vision Assist
A camera that tells you what it sees.
Real-time scene description, spoken out loud
Notes: Hi everyone. Vision Assist is a small project with one goal: point a camera at a room and have it tell you, in plain English, what is in front of you. I'll show the idea, how it works, and be honest about what is still unfinished.

## Slide 2
The everyday problem
Imagine walking into a room you can’t see
Take Sam, walking into a new meeting room.
There’s a table, some chairs, and someone standing close by. A camera can see all of it. But a silent video helps no one who can’t look at a screen.
“Very close: a person in front, two chairs on the left.”
What Vision Assist says instead
(Sam is an illustrative example, not a user study.)
Notes: Picture someone walking into an unfamiliar room, or just someone whose hands and eyes are busy. A camera sees everything, but a video feed doesn't say anything. This is the gap we wanted to close. Sam is just an example person, not a real user study.

## Slide 3
The idea in one picture
What it sees, and what it says
chair 88%
person 94%
chair 81%
Live camera view (illustration)
Then it says…
very close: a person in front, two chairs on the left
on screen and out loud
Notes: This is a drawn illustration of the live view, not a real screenshot. Each green box is something the model found, with how sure it is. Underneath is the sentence we turn those boxes into. Notice it says where things are, and how close.

## Slide 4
Three simple steps
How it works: see, decide, say
1
See
A YOLO model looks at the latest camera frame and finds objects, each with a box and a confidence.
2
Decide
We work out left, in front or right, and how close, then smooth out flicker.
3
Say
Everything becomes one short sentence, shown on screen and read aloud.
Notes: Under the hood there are three jobs. See: a model called YOLO finds objects in each frame. Decide: we work out where each thing is and how close, and clean up the noise. Say: we turn it into one short sentence and speak it. Same flow for the website and the desktop app.

## Slide 5
Making it useful, not just accurate
Where is it, and how close?
Left, front, right
on the left
in front
on the right
The frame is split into three equal parts, based on the middle of each object.
How close
Very close fills a quarter of the frame or more
Near fills about a twelfth or more
Far anything smaller
It also groups things (“two chairs”), handles plurals (people, knives), reads the closest objects first, and keeps it to four phrases at most.
Notes: A list of objects isn't very helpful. 'Chair' tells you little; 'chair on your left' is useful. We split the picture into thirds for left, front and right. For distance we use how much of the frame the object fills. That's an estimate, not a measurement, and I'll come back to that.

## Slide 6
Calm by design
Why it doesn’t chatter
It only mentions what’s stable
An object must appear in at least 3 of the last 5 frames. A one-frame glitch never gets spoken, and two people stay “two people” even if one blinks out for a moment.
It waits its turn
At least 3 seconds between updates. The same sentence isn’t repeated for 15 seconds. A sentence already being spoken is never cut off.
Notes: If we spoke every frame, you'd hear constant nonsense, because detections flicker. So we added two guardrails. An object must show up in at least three of the last five frames before we mention it. And we wait a few seconds between updates and don't repeat ourselves. Think of it as a polite narrator rather than a nervous one.

## Slide 7
The website
Try it in the browser
Vision Assist
LIVE
Capture
Stop live
Illustration of the page
Webcam first Starts on load; stop and restart any time.
Live or one-shot Continuous mode with boxes, or capture a single frame.
Hear it Browser speech reads each new description.
Upload a photo Analyze it, then remove it with one click.
Notes: This is the web page, drawn as a mock-up. The camera starts when you open it. Press Start live and it describes continuously with boxes on the video; Capture analyses one frame. You can also upload a photo, and there's a Remove button to clear it. Frames are shrunk to 640 pixels in the browser so it stays quick.

## Slide 8
For the curious
Under the hood
detector.py
Runs the YOLO model
camera.py
Always keeps the newest frame
scene.py
Turns boxes into a sentence
speaker.py
Talks, without nagging
api.py
Serves the page and the API
app.py
The desktop window
Talk to it
POST /api/process Send a photo, get back a sentence and the boxes. /lens A bigger model with about 4,500 object types, for still photos.
Notes: For anyone who wants the plumbing. One Python process serves both the page and the analysis API. Each file has one job, which keeps it easy to change. The photo lens page uses a bigger model that knows far more objects, but it's slower, so live video keeps the fast one.

## Slide 9
Performance
Fast enough to feel live
Chart: Time per frame on a CPU (ms)
| yolov8n (fastest) | yolov8s (default) | yolo11s
Milliseconds per frame | 73 | 114 | 126
~0.15 s
from camera frame to sentence, through the API (about 140–160 ms)
Need it faster? Use the smaller yolov8n model.
Notes: On a normal CPU, with no graphics card, the default model takes about a tenth of a second per frame, and roughly a seventh of a second including the trip through the API. That's quick enough to feel live. If you need more speed, switch to the smaller yolov8n model.

## Slide 10
Being honest
What it can’t do yet
Not tested on a live webcam yet
So far: 11 passing tests and a check on a real photo. Real-world use comes next.
Distance is a guess
It comes from how big the box is, not from a real measurement.
It only knows what it was trained on
Unfamiliar objects can be missed or named differently.
A prototype, not a safety device
Please don’t rely on it to get around.
Notes: I want to be upfront. We've tested the logic with automated tests and checked the API on a real photo, but we haven't yet run it with a real webcam, which is the next thing to do. Distance is a guess from box size, and the model only knows the kinds of objects it was trained on. This is a prototype, not a safety device, and nobody should rely on it to navigate.

## Slide 11
WHAT’S NEXT
From working demo to something you can trust
Try it on a real webcam
Desktop app first, then the website.
Tune it with real use
Adjust thresholds for what feels natural to hear.
Get real feedback
Ask people who would actually use it.
Thank you. Questions?
Notes: That's Vision Assist: a simple idea, a working prototype, and a clear list of what to do next. The most valuable thing now is trying it for real and hearing from people who would use it. Happy to take questions.